## Slide 1
SiNK 2026 · RESEARCH PRESENTATION
01
Toward a battery digital twin
Phase 1: reliable cyclic voltammetry evidence
Cheritha Kaiwar · Prajwal S · Karan Koder
Under the guidance of Dr. Manjunatha C.
RV College of Engineering, Bengaluru
Notes: Title and authors supplied by the project team. Scope: implemented CV quality layer, with future battery-health validation planned.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 2
Problem statement
SiNK 2026 · RESEARCH PRESENTATION
02
Industry needs battery diagnostics grounded in reliable measurements.
A CV trace can have missing units or acquisition details.
A scan boundary can cut off a peak and make its potential unknowable.
A health model trained on generated labels cannot establish physical-cell accuracy.
Engineering need: check the evidence before reporting features or health estimates.
Notes: Industrial context: NREL Battery Lifespan research, https://www.nrel.gov/transportation/battery-lifespan.html. CV and model limitations are findings from this repository.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 3
Existing solutions and our contribution
SiNK 2026 · RESEARCH PRESENTATION
03
Battery management | Uses operating voltage, current and temperature to estimate state.
Potentiostat software | Plots CV scans and provides peak and baseline analysis.
Health prediction research | Trains models on features paired with measured capacity.
This Phase 1 prototype | Keeps CV acquisition order, checks support for features, and shows why a value is withheld.
Notes: Sources: NREL https://www.nrel.gov/transportation/battery-lifespan.html ; Gamry Echem Analyst manual https://www.gamry.com/assets/Uploads/EchemAnalystSoftwareManual.pdf ; battery SoH ML on labeled cells https://arxiv.org/abs/2102.00837 . No claim of unique invention or superiority over existing CV tools.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 4
Research question and scope
SiNK 2026 · RESEARCH PRESENTATION
04
Detect when a CV scan does not support a reported feature
Notes: Phase 1 is implemented in the repo. Phase 2 requires repeated measurements and independent capacity labels. Phase 3 requires a calibrated model that updates for an identified physical battery. Figure is generated from research/generate_conference_figures.py. SINk 2026 organiser theme context: https://www.linkedin.com/posts/dr-vishal-chaudhary_schedule-activity-7508161441263304704-ga_Y . The fit is electrochemical sensing linked to interpretable decisions, with an energy application.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 5
Methodology: CV quality gate
SiNK 2026 · RESEARCH PRESENTATION
05
Notes: Data flow: preserve ordered CSV; require explicit units in the live API; check forward and return branch, closure and interior extrema; report only supported descriptors. The synthetic RF model is a separate dataset and not connected to the measured trace. Figure generated from repository source.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 6
Experimental input: one reported CV sweep
SiNK 2026 · RESEARCH PRESENTATION
06
21 measured values
Team reports a real CV setup.
Approximately room temperature.
Electrodes reported: graphite, platinum and Ag/AgCl. Roles not documented.
Scan rate and current unit not recorded in the CSV.
Notes: Source: attached_assets/14,12csv_1765724360390.csv and research/experimental_metadata.json. Current is plotted in µA only under a provisional assumption that the source numbers are amperes. Team reports experimental origin, but original instrument export is unavailable.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 7
Measured result: peak separation withheld
SiNK 2026 · RESEARCH PRESENTATION
07
Quality: limited
Apparent extrema sit at the scan limits.
The true peak positions may lie beyond the voltage window.
The system leaves ΔEp blank and gives the reason.
Notes: Source: supplied 21-point CSV, analyzed by research/cv_sensor_study.py and the live API. The signed path integral is approximately -1.75e-7 A·V under the provisional ampere assumption; it is not charge, energy or capacity.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 8
Controlled test: sensitivity to current noise
SiNK 2026 · RESEARCH PRESENTATION
08
At 10% noise
10 mV
median absolute error
30.5 mV
95th percentile error
Simulation only; 200 replicates per level
Notes: Source: research/results/sensor_report.json, seed 20260926. Gaussian peak simulation: +/-0.10 V peaks, 3 microamp amplitude, 10 mV sampling. Independent Gaussian current noise. At 10% current noise: median absolute separation error 10 mV, empirical 95th percentile 30.5 mV across 200 seeded replicates. This measures software extractor sensitivity under one signal model. It is not an instrument error specification or physical battery accuracy. The single experimental scan has 50 mV potential increments and no reference peak or repeats, so physical sensing accuracy is unknown.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 9
Random Forest regression metrics
SiNK 2026 · RESEARCH PRESENTATION
09
Generated-data random split: R² 0.9976, RMSE 1.01 points, MAE 0.75 points
Notes: Source: ml/training_data.csv and research/conference_figures/figure_metrics.json. Features were generated from the synthetic SoH trajectory. Random row split: RMSE 1.0072 SoH points, MAE 0.7460 points, R2 0.997608. Last 30 cycles held out: RMSE 14.7183 points, MAE 13.1128 points, R2 -3.771964. R2 is a regression fit measure, not classification accuracy. Neither test validates a physical cell. The live API does not run this model.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 10
Conclusion
SiNK 2026 · RESEARCH PRESENTATION
10
Phase 1 provides a working CV evidence layer.
The prototype preserves the reported experimental trace and checks sweep quality.
It correctly withholds peak separation for boundary-limited data.
The simulation tests extraction sensitivity; the synthetic model audit does not validate SoH.
Notes: Conclusion limited to implemented software behavior and one team-reported experimental trace. The project has no independently measured capacity labels, so it cannot claim health prediction accuracy or a complete digital twin.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 11
Future scope
SiNK 2026 · RESEARCH PRESENTATION
11
Phase 2: physical validation
Recover instrument exports, electrode roles, material identity, units and scan rate.
Repeat CV on identified cells and pair each sweep with measured discharge capacity.
Test repeatability and any SoH model on entire cells held out from training.
Phase 3: operational twin
Calibrate a battery-specific state model, update it from new data, and verify it over time.
Notes: Future work proposal, not achieved results. The original 21-point CSV has no capacity target or complete acquisition metadata. Proposed physical validation follows the principles of separated cells and independently measured outcomes.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 12
References
SiNK 2026 · RESEARCH PRESENTATION
12
Project data and methods. Battery-digital-twin repository: experimental CSV, metadata record, sensor study, and synthetic audit (2026).
NREL. Battery Lifespan: diagnostics and model-based battery health research. nrel.gov/transportation/battery-lifespan.html
Elgrishi et al. A Practical Beginner’s Guide to Cyclic Voltammetry. Journal of Chemical Education 95 (2018). DOI: 10.1021/acs.jchemed.7b00361
Gamry Instruments. Echem Analyst software manual: cyclic voltammetry analysis. gamry.com/assets/Uploads/EchemAnalystSoftwareManual.pdf
"Battery digital twins: Perspectives on the fusion of models, data and artificial intelligence." Energy and AI 1 (2020). DOI: 10.1016/j.egyai.2020.100016
"Machine learning pipeline for battery state of health estimation" (2021). arXiv:2102.00837
Notes: Full URLs: https://www.nrel.gov/transportation/battery-lifespan.html ; https://pubs.acs.org/doi/10.1021/acs.jchemed.7b00361 ; https://www.gamry.com/assets/Uploads/EchemAnalystSoftwareManual.pdf ; https://doi.org/10.1016/j.egyai.2020.100016 ; https://arxiv.org/abs/2102.00837 .
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 13
Electrode materials reported by the team
SiNK 2026 · FIGURE APPENDIX
13
Notes: The team reported graphite, platinum and Ag/AgCl. Exact roles, material and electrolyte are not documented. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 14
Potential sequence
SiNK 2026 · FIGURE APPENDIX
14
Notes: Same team-reported 21-point experimental trace. Time and scan rate unavailable. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 15
Current sequence
SiNK 2026 · FIGURE APPENDIX
15
Notes: Same team-reported experimental trace; current unit provisional. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 16
Forward and return current difference
SiNK 2026 · FIGURE APPENDIX
16
Notes: Derived from the same 21 points. Descriptive curve, no mechanism attribution. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 17
Potential sampling steps
SiNK 2026 · FIGURE APPENDIX
17
Notes: Step size cannot determine scan rate without timestamps. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 18
Signed path integral
SiNK 2026 · FIGURE APPENDIX
18
Notes: A·V under the provisional ampere interpretation. This is not charge or energy. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 19
Generated SoH trajectory
SiNK 2026 · FIGURE APPENDIX
19
Notes: From ml/training_data.csv; no measured capacity values. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png

## Slide 20
Synthetic feature correlations
SiNK 2026 · FIGURE APPENDIX
20
Notes: Features derive from generated SoH labels; correlations are not physical discovery. Figure generated by research/generate_conference_figures.py from repository data.
Logo source: https://d2lk14jtvqry1q.cloudfront.net/media/large_89_9b01402b5b_926235f86d.png